## Slide 1: Section I: Digital System Analysis and Review
CEG 360/560; EE 451/651
Digital System Design
Dr. Travis Doom, Assistant Professor
Department of Computer Science and Engineering
Wright State University
Thanks to M. Mano, J. Wakerly, R. Haggard

## Slide 2: Acknowledgements
These slides were developed with the aid of examples found in:
  “Logic and Computer Design Fundamentals” - M. Morris Mano
  “Digital Design: Principles and Practices” - John Wakerly
The original version of many of these slides were kindly provided by:
  Dr. Roger L. Haggard et al.
  Prentice Hall, Inc.

## Slide 3: Outline
Review of Combinational Logic Concepts
What is Sequential Logic?
  Bi-stable Logic Elements and Metastability
Basic Sequential Devices
  Flip-flops: Type, Function, and Structure
  Characteristic Equations
The Clocked Synchronous State Machine (CSSM)
  Analysis of State Machines
    General structure, Analysis procedure
    CSSM Models: Mealy Vs. Moore
  Methods of Representation
    State tables and diagrams
  Timing
    Calculating Setup Time, Hold Times, and Maximum clock rate

## Slide 4: Logic Devices
Logic devices divide into two major types:
Combinational Logic
  Current output depends on current input only
  Examples: gates, decoders, multiplexors (MUXs), ALUs
  Familiarity with combinational logic is a course prerequisite
Sequential Logic
  Current output depends on past inputs as well as current input
  Thus has a memory (usually called the state)
  Examples: latches, flip-flops, state machines, counters, shift registers

## Slide 5: Basic Logic Gates
AND gate
  Output Z = 1 only when inputs A and B are both 1
OR gate
  Output Z = 1 only when inputs A or B or both are 1
NOT gate or inverter
  Output Z = 1 only when input A is 0
Simple alone, but combine a few million gates properly and you have a computer!
A
B
Z
A
B
Z
Z
A

## Slide 6: Gate Symbols
OR
NOR
AND
NAND
INVERTER
BUFFER
Exercise: show that the equivalent gates do the same function

## Slide 7: Schematic diagram/Logic Diagram
Good Design Practices include:
  Bubble-to-Bubble logic
  All wires are either horizontal or vertical
  Wires are connected at “T” intersections
  Wires are not connected at “X” intersections
Schematic diagrams should include
  IC-Type-Logic Family
  Pin numbers- Pin Diagram
  Reference designator- Unit Number
/A
/ B
F
F
/A
/B
74LS04
74LS04
74LS00
74LS00
74LS00
1
2
3
4
1
2
3
4
5
6
10
9
8
U1
U1
U1
U2
U2
Wires connected
Wires not connected
Logic Diagram
Schematic Diagram

## Slide 8: Bubble-to-Bubble Logic Design
Purpose : To make it easy to understand the function of the Logic circuit
ERROR
/ FAIL
/ OVERFLOW
ERROR
/ FAIL
/ OVERFLOW

## Slide 9: Digital Devices
Analog characteristics
  Continuous signal levels
  Very small, smooth level changes
Digital characteristics
  Discrete signal levels (voltage usually)
  Two levels: on/off, high/low 1/0 (binary)
  Disjoint or quantized level changes
Digital Concepts and Devices
  Digital Design also called Logic Design
  Logic Gates - the most basic digital devices
  Digital devices have analog electronic aspects
    Exercise: list some of these aspects
t
v
v
t

## Slide 10: Electronic Aspects of Digital Design
Vin low  Ib = 0
  transistor cut off: Vout = Vcc
Vin high  Ib > 0
  transistor “on”: Vout = GND
Vin
Vout
GND
Vcc
Rc
Rb
Vcc
VIHmin
VOLmax
Vin
VOLmax
VOHmin
GND
Vcc
VCESat
Vout
Abnormal
except for
switching
VOLmax: max output voltage in low state
VOHmin: min output voltage in high state
VILmax: max input voltage recognized as low
VIHmin: max input voltage recognized as high

## Slide 11: Electronic Aspects of Digital Design
Digital devices are built with analog components
A range of voltages associated with each logic value ( 0 or 1 )
Noise margin : The difference between the range boundaries
  in low state = VILmax - VOLmax = 1.5 V - 0.1 V= 1.4 V for 5V CMOS
  in high state = VOHmin - VIHLmin = 4.9 V - 3.5 V= 1.4 V for 5V CMOS
Voltage
Outputs
Noise Margin
Inputs
Logic 0
Logic 0
Logic 1
Logic 1
Invalid

## Slide 12: Electronic Aspects of Digital Design
Logic gates Specifications : - Conditions under which the digital device produces and recognizes logic signals within the appropriate range.
- Examples : - Power-supply voltage - Temperature - Loading - Frequency
Manufacturer specifications ( data sheets )

## Slide 13: Propagation Delay
The delay time between input transitions and the output transitions due to the propagation delay of the the logic gates.
tp of a signal depends on the signal path inside the logic circuit
For a logic gate tpLH may not equal tpHL
tp is specified in the manufacturer data sheets of the IC’s
Example : -The time delay for 74x00 in nanoseconds for three logic Families: Typical Maximum tpLH tpHL tpLH tpHL 74LS00 9 10 15 15 74HCT00 11 11 35 35 74ACT00 5.5 4.0 9.5 8.0
To find tp for a signal, add the propagation delays of all gates along the path of the signal

## Slide 14: Timing Diagrams
Y
X
X
Y
tpLH(XY)
tpHL(XY)
trise
tfall
Actual Timing Diagram
Functional Timing Diagram
X
Y
Functional timing diagrams do not show exact delays.
“lining up” everything allows the diagram to display more clearly which functions are performed in response to which action
  Illustrates operation, but does not specify upper and lower limits
  Not always sufficient for a real design

## Slide 15: Decoder
Multiple-input/multiple-output device.
Decoder - Inputs (n) < outputs (m).
Encoder - Inputs (n) > outputs (m)
Converts input code words into output code words.
One-to-One mapping : - Each input code produces only one output code.
Input codes : - Binary Code - Gray Code - BCD Code - Your Code !
input code
enable inputs
output code
DECODER
input code
output code
ENCODER

## Slide 16: Binary Decoder
n-to-2^n decoder: n inputs and 2^n outputs.
Input code : Binary Code.
Output code : 1-out-of-2^n , One output is asserted for each input code.
Example : n=2, 2-to-4 decoder Inputs Outputs EN I1 I0 Y3 Y2 Y1 Y0 0 x x 0 0 0 0 1 0 0 0 0 0 1 1 0 1 0 0 1 0 1 1 0 0 1 0 0 1 1 1 1 0 0 0
EN
I0
I1
Y0
Y1
Y2
Y3

## Slide 17: Comparators
Compares Two binary words and indicate if they are equal
Advanced Comparators :
1-bit Comparator : XOR gate , the Output is 1 if A<>B
A
Comparator
OUTPUT
B
A
Comparator
A=B
B
A>B
A<B
A
B
F

## Slide 18: Iterative Combinational Logic
Iterative logic array: A device consisting of identical sub-circuits connected together in a chain to perform a larger overall function
Iterative Comparator : cascaded 1-bit comparators
1-bit comparator : Function Table EQI X Y EQO 0 x x 0 1 0 0 1 1 0 1 0 1 1 0 0 1 1 1 1
X
Y
EQI
EQO
X
Y
EQI
EQO
X0
Y0
EQ0 =1
EQ1
X
Y
EQI
EQO
X1
Y1
EQ1
X
Y
EQI
EQO
X(N-1)
Y(N-1)
EQN
EQ1(N-1)

## Slide 19: MSI Arithmetic Logic Units (ALU )
ALU performs Arithmetic and Logical Functions - A , B : 4 bits inputs - S3,S2,S1,S0 : Function select - M=0 : Arithmetic operations +=Plus , - = Minus M=1 : Logical operations : += OR , . =AND
Example : Inputs Functions S3 S2 S1 S0 M=0 M=1 0 0 0 0 F= A-1+CIN F=A’ 0 1 1 0 F= A-B-1+CIN F=A XOR B’ 1 0 0 1 F= A+B+CIN F=A XOR B 1 0 1 1 F=(A OR B)+ CIN F=A+B 1 1 0 0 F= A+A+CIN F= 0000 1 1 1 1 F=A+CIN F=A
S1
S2
S3
F1
F2
M
CIN
A0
S0
F0
B0
74x181
F3
COUT
A1
B1
A2
B2
A3
B3
A=B
P
G

## Slide 20: Multiplexers
Multiplexing: transmitting large number of signals over a small number of channels or lines
Digital multiplexer (MUX): selects one of many input lines and directs it to a single output (often a bus or “party line”).
Selection lines controls the selection of a particular input
m-bit 2n x 1 multiplexer:
  n selection lines, 2n m-bit inputs, 1 m-bit output.
Example : 4-to-1 line multiplexer: Function Table : S1 S0 Y 0 0 I0 0 1 I1 1 0 I2 1 1 I3
I0
Y
S1
S0
Inputs
Output
Select
I1
I2
I3

## Slide 21: Implementing Logic Functions
Any n-variable logic function can be implemented using a 2n-to-1 MUX
  (In fact, MUXs are a universal device! Any combinational function can be implemented using only MUXes).
The inputs variables are connected to the select input.
The function value for each input combination (0 or 1) is connected to the corresponding input of the MUX
Example:
Row X Y F 0 0 0 0 1 0 1 1 2 1 0 0 3 1 1 1
I0
Y
S1
S0
F
I1
I2
I3
X
Y
0
1
0
1

## Slide 22: Functional Decomposition
Effective way for using MUX to implement Logic Functions.
n-variable truth table can be simplified using any MUX :
  Use one or more variables as control inputs
  Decompose the remaining logic function in terms of the remaining inputs
  For 3-variable Logic Function , the decomposed truth table is : Row X Y Z F 0,1 0 0 x F00(Z) 2,3 0 1 x F01(Z) 4,5 1 0 x F10(Z) 6,7 1 1 x F11(Z) Values of Fxx(Z) = 0 or 1 or Z or Z’
I0
Y
S1
S0
F
I1
I2
I3
X
Y
F00(Z)
F01(Z)
F10(Z)
F11(Z)

## Slide 23: Demultiplexers
Demultiplexer (DMUX) performs the opposite function of a MUX.
A digital Demultiplexer receives input data on a single input and transmits it on one of 2^n possible outputs according to the value of the n select inputs
MUX/DMUX are used in data transmission
Source Destination
MUX
DMUX
A
B
C
A
B
C
Select
Select
BUS

## Slide 24: Programmable Logic Devices
PLDs are generic logic devices capable of implementing a wide range of combinational (and sequential) functions.
  O0 = F0(x0…xn)
  O1 = F1(x0…xn)
  …
  Om = Fm(x0…xn)
Combinational
PLD
m outputs
n inputs

## Slide 25: Outline
Review of Combinational Logic Concepts
What is Sequential Logic?
  Bi-stable Logic Elements and Metastability
Basic Sequential Devices
  Flip-flops: Type, Function, and Structure
  Characteristic Equations
The Clocked Synchronous State Machine (CSSM)
  Analysis of State Machines
    General structure, Analysis procedure
    CSSM Models: Mealy Vs. Moore
  Methods of Representation
    State tables and diagrams
  Timing
    Calculating Setup Time, Hold Times, and Maximum clock rate

## Slide 26: Sequential Logic Definitions
STATE- A collection of state variables whose values at any one time contain all the information about the past values necessary to account for future behavior.
Example: A TV tuner could have a current channel stored internally, so the next channel can be predicted as a function of the inputs, i.e. the UP button increases the channel by one, the DOWN button decreases the channel by one. What is the state of this TV tuner?
Digital sequential logic
  State variables are binary values
  Circuit with n binary state variables has 2n possible states
  Also known as a finite state machine (FSM).
  Changes usually synchronized with a system clock

## Slide 27: Bistable Element
The simplest possible feedback sequential logic circuit is shown below:
It is bistable because it has two stable states:
  State 1: If Q (Q=Vout1=Vin2) is high, the bottom inverter output (/Q =Vout2=Vin1) is low, which keeps the top inverter output Q high.
  State 2: If Q is low, the bottom inverter output /Q is high, which keeps the top inverter output Q low.
Vin1
Vin2
Vout1
Vout2
Q
/Q

## Slide 28: Analog Analysis of a Bistable
Q Vout1
Vin2
Vin1
Vout2 /Q
Vout1 =Vin2
Top Inverter alone
Bottom Inverter alone
Complete Bistable
Vin1
=Vout2
Stable High
Stable Low
Metastable

## Slide 29: Bistable Devices and Metastability
There are not two stable states, but three (a problem!)
A metastable point occurs when both outputs are halfway between high and low, the resulting output is not a valid logic level.
Metastability could last forever, but noise usually pushes towards a stable state (HIGH or LOW).
Noise in a bistable state returns it to the same stable state
Every input pulse must remain stable “long enough”
  This is the minimum pulse width for the bistable element
Analogous to a ball on a hill:
Strong kick (wide pulse)? Weak kick?
Moderate kick?
Stable High
Stable Low
Metastable

## Slide 30: S-R Latch
S
R
Q
/Q
0
0
1
1
0
1
0
1
Last Q
0
1
0
Last /Q
1
0
0
S
R
Q
/Q
S
R
Q
Q
Schematic
Symbol
Hold
Reset
Set
ILLEGAL
Function Table
Set
Reset
Characteristic Equation:
Q(t+1) = S + R’Q(t)
Consider:
  Timing Diagram
  Propagation delay
  Minimum pulse width
  Oscillation

## Slide 31: /S-/R Latch
/S
/R
Q
/Q
0
0
1
1
0
1
0
1
1
1
0
last Q
1
0
1
last /Q
/S
/R
Q
/Q
S
R
Q
Q
ILLEGAL
Set
Reset
Hold

## Slide 32: S-R Latch with Enable
S
Q
/Q
0
0
1
1
X
R
0
1
0
1
X
Last Q
0
1
1
Last Q
Last /Q
1
0
1
Last /Q
Q
/Q
S
R
C
C
1
1
1
1
0
S
R
Q
Q
C
Only sensitive to S and R when enabled (C=1)
Same oscillation problem
How does C effect the
minimum pulse width?

## Slide 33: D Latch
D
C
Q
Q
Q
/Q
D
C
C
D
Q
/Q
1
1
0
0
1
X
0
1
Last Q
1
0
Last /Q
Characteristic Equation:
Q(t+1) = D
Store a data bit, not set/reset
The “Transparent” latch
No illegal operation problem

## Slide 34: Outline
Review of Combinational Logic Concepts
What is Sequential Logic?
  Bi-stable Logic Elements and Metastability
Basic Sequential Devices
  Flip-flops: Type, Function, and Structure
  Characteristic Equations
The Clocked Synchronous State Machine (CSSM)
  Analysis of State Machines
    General structure, Analysis procedure
    CSSM Models: Mealy Vs. Moore
  Methods of Representation
    State tables and diagrams
  Timing
    Calculating Setup Time, Hold Times, and Maximum clock rate

## Slide 35: Types of Sequential Logic
An Asynchronous Sequential Circuit uses ordinary gates and feedback loops to implement “memory” in a logic circuit.
  Meeting minimum pulse width requirements may be tricky
A Synchronous Sequential Circuit uses flip-flops (internally, an asynchronous sequential device) to form useful sequential logic functions or applications.
  The state variables and outputs of a synchronous system change with respect to a controlling clock signal
  Meeting minimum pulse width requirements is simplified by restating all timing constraints in terms of the clock signal

## Slide 36: Sequential Logic Definitions
Clock - the master timing element behind the state changes of most sequential circuits.
  a clock signal is active high if the state changes occur at the rising edge (for edge triggered devices) or in the logic 1 state (for pulse-triggered devices)
  active low if state changes occur at the falling edge or in the logic 0 state.
Clock Period - time between successive transitions in the same direction
Clock Frequency - reciprocal of the clock period
Clock Tick - the first edge or pulse in a clock period, or the period itself
Duty Cycle - the percentage of time that a clock is at its assertion level

## Slide 37: Clock Characteristics
Period
tH
tL
State change
Active High
Period
tH
tL
State change
Active Low
Duty Cycle = tL/Period
Frequency= 1/Period
Duty Cycle = tH/Period

## Slide 38: Master/Slave S-R Flip-Flop
S
C
Q
/Q
S
R
Q
Q
C
R
S
R
Q
Q
C
S
R
Q
Q
C
S
C
Q
/Q
X
0
0
1
1
Last Q
Last Q
0
1
undef.
Last /Q
Last /Q
1
0
undef.
R
X
0
1
0
1
0
“Pulse-triggered” S-R flip-flop
Multiple signals may conflict
Ideally, inputs are held for the
entire enable pulse
Only one state change/pulse

## Slide 39: Master/Slave J-K Flip-Flop
J
K
Q
Q
C
J
C
Q
/Q
X
0
0
1
1
Last Q
Last Q
0
1
Last /Q
Last /Q
Last /Q
1
0
Last Q
K
X
0
1
0
1
0
C
Q
/Q
S
R
Q
Q
C
S
R
Q
Q
C
J
K
Fixes S=R=1 problem, now toggles
1/0s catching - gate propagation
delays complicate timing

## Slide 40: Positive-Edge-Triggered D Flip-Flop
D
>CLK
Q
Q
D
C
Q
D
C
Q
Q
D
CLK
Q
/Q
D
CLK
Q
/Q
0
1
X
X
0
1
0
1
Last Q
Last Q
1
0
Last /Q
Last /Q
Master
Slave
QM
Device samples inputs and changes state
only on a clock edge.
Simplifies the meeting of setup/hold times.
Master FF - transparent on CLK’ (entire pulse)
Slave FF - transparent on CLK (master fixed)

## Slide 41: Negative-Edge-Triggered D Flip-Flop
D
C
Q
D
C
Q
Q
D
CLK
Q
/Q
D
CLK
Q
/Q
0
1
X
X
0
1
0
1
Last Q
Last Q
1
0
Last /Q
Last /Q
D
>CLK
Q
Q

## Slide 42: Edge-Triggered J-K Flip-Flop
J
K
Q
Q
>CLK
Q
D
>CLK
Q
Q
/Q
CLK
J
K
C
Q
/Q
J
X
X
0
0
1
1
Last Q
Last Q
Last Q
0
1
Last /Q
Last /Q
Last /Q
Last /Q
1
0
Last Q
K
X
X
0
1
0
1
0
1
Q(t+1) = J Q(t)’ + K’ Q(t)

## Slide 43: T (toggle) Flip-Flop
A T flip-flop changes state on every clock tick (if enabled)
Possible circuit designs
  T without enable
  T with enable
D
>CLK
Q
Q
Q
/Q
J
K
Q
Q
>CLK
1
Q
/Q
J
K
Q
Q
>CLK
T
Q
/Q
D
>CLK
Q
Q
Q
/Q
T
Q(t+1) = Q’(t)
Q(t+1) = T Q(t)’ + T’ Q(t)

## Slide 44: Types Latches and Flip-flops
Common Latches
  S-R Latch
  /S-/R Latch
  S-R Latch with Enable
  D Latch
Common Flip-flops
  Edge-Triggered D Flip-Flop
  Master/Slave S-R Flip-Flop
  Master/Slave J-K Flip-Flop
  Edge-Triggered J-K Flip-Flop
  T Flip-Flop

## Slide 45: Characteristic Equations
Describe the next state of a flip-flop as function of current state and inputs: Q(t+1) = f (Q(t), inputs)
  t+1 represents the next clock tick
  t represents the current clock tick
  t-1 represents the previous clock tick
  and so on...
Derived from basic function table for a given flip-flop type
Very useful in state machine analysis and design

## Slide 46: Characteristic Equations
D latch or flip-flop
present next
input state state
D Q(t) Q(t+1)
________________________________________
0 0 0
0 1 0
1 0 1
1 1 1
________________________________________
Characteristic Equation:
Q(t+1) = D
S-R latch
S R Q(t) Q(t+1)
____________________________________________________
0 0 0 0
0 0 1 1
0 1 X 0
1 0 X 1
1 1 X X
__________________________________________________
Characteristic Equation:
Q(t+1) = S + R’ Q(t)

## Slide 47
J-K flip-flop
J K Q(t) Q(t+1)
_______________________________________________________
0 0 0 0
0 0 1 1 = hold
0 1 0 0
0 1 1 0 = reset
1 0 0 1
1 0 1 1 = set
1 1 0 1
1 1 1 0 = toggle
______________________________________________________
Characteristic Equation:
Q(t+1) = J Q(t)’ + K’ Q(t)
T flip-flop with enable
T Q(t) Q(t+1)
________________________________________
0 0 0
0 1 1
1 0 1
1 1 0
________________________________________
Characteristic Equation:
Q(t+1) = T Q’(t) + T’ Q(t)
Characteristic Equations

## Slide 48: Characteristic Equations Summary
Device Type Characteristic Equation
___________________________________________________________________________________________________________________
S-R latch Q(t+1) = S + R’ Q(t)
D latch Q(t+1) = D
Edge-triggered D flip-flop Q(t+1) = D
Master/slave S-R flip-flop Q(t+1) = S + R’ Q(t)
Master/slave J-K flip-flop Q(t+1) = J Q(t)’ + K’ Q(t)
Edge-triggered J-K flip-flop Q(t+1) = J Q(t)’ + K’ Q(t)
T flip-flop Q(t+1) = Q(t)’
T flip-flop with enable Q(t+1) = T Q(t)’ + T’ Q(t)

## Slide 49: What Are Flip-flops?
Common asynchronous (feedback) sequential circuits
Latch
  Single-bit storage (memory)
  Changes state at any time due to input change
  Must guarantee a minimum pulse width to avoid metastability
  Fast and cheap (small # of transistors)
  Often used in high speed microprocessor design
Flip-flop
  Also single-bit storage
  Changes state ONLY when a clock edge or pulse is applied
  Uses setup and hold times before and after the clock pulse to avoid metastability
  Clocking simplifies the design process

## Slide 50: Flip-flop Timing
Combinational
tpd,min - minimum propagation delay, input to output
tpd,max - maximum propagation delay, input to output
Latch
tpd,min - minimum propagation delay, input to output
tpd,max - maximum propagation delay, input to output
tw - minimum pulse width, input to input
Flip-flip
tpd, min - minimum propagation delay, CLK to output
tpd, max - maximum propagation delay, CLK to output
tsetup - required time of stable input before CLK, input before CLK
thold - required time of stable input after CLK, input after CLK
J
K
Q
Q
>CLK
tpd
tsetup, thold

## Slide 51: Asynchronous Inputs
Most flip-flops have two asynchronous/direct inputs
Preset and Reset (or Clear)
Directly set or reset the /S-/R latches
Operate independent of clock
Good design practice dictates:
  NEVER use asynchronous inputs for logic functions, only for system initialization to a known state
Why? Recall:
  Synchronous circuits: behavior of circuit depends on the value of the signals at discrete points in time, determined by a control signal (clock)
  Asynchronous circuits: behavior of circuit depends on the order in which the inputs signals change (changes can occur at any time)

## Slide 52: Outline
Review of Combinational Logic Concepts
What is Sequential Logic?
  Bi-stable Logic Elements and Metastability
Basic Sequential Devices
  Flip-flops: Type, Function, and Structure
  Characteristic Equations
The Clocked Synchronous State Machine (CSSM)
  Analysis of State Machines
    General structure, Analysis procedure
    CSSM Models: Mealy Vs. Moore
  Methods of Representation
    State tables and diagrams
  Timing
    Calculating Setup Time, Hold Times, and Maximum clock rate

## Slide 53: Clocked Synchronous State-machine Analysis
Analysis
  How does a given circuit work? What does it do?
  How do input sequences map to output sequences?
Clocked synchronous state-machine
  Clocked: storage elements (flip-flops) use a clock input
  Synchronous: all flip-flops use the same clock signal
State-machine types
  Mealy Machine (most general type):
    Next state = F ( current state, inputs )
    Output = G ( current state, inputs )
  Moore Machine:
    Next state = F ( current state, inputs )
    Output = G ( current state )

## Slide 54: Clocked Synchronous State-machine Model
Next-state
Logic
F
State
Memory
clock
Output
Logic
G
excitation
inputs
clock
current state
outputs
(Mealy machine)
Moore Machine
State memory:
Usually edge-triggered
D or JK flip-flops

## Slide 55: Basic Analysis of State Machines
Determine next-state and output functions F and G
Use F and G to construct a state/output table
Draw a graphical representation of the state/output table
  State Diagram
    Common for small designs
    Similar to a finite automata
  Algorithmic State Machine (ASM) Chart
    Common for larger designs
    Similar to a flowchart
  Timing Diagram
    Common for all designs

## Slide 56: Detailed Analysis of State Machines
Analyze the combinational logic to determine flip-flop input (excitation) equations:
  Di = Fi (Q(t), X(t))
  The input to each flip-flop is based upon current state and primary inputs
Substitute excitation equations into flip-flop characteristic equations, giving transition equation:
  Qi(t+1) = Hi( Di )
Construct a state table from the transition equations
Find output equations:
  Z(t) = G (Q(t), X(t))
  The primary outputs are based upon the current state and primary inputs
  Add output values to the state table
  Provide meaningful names for the states in state table, if possible
  The graphical representation of state table is called a state diagram
Analyze timing requirements

## Slide 57: State Diagram
B
1
0, 1
A
0
1
B
1 / 1
0 / 1, 1 / 0
A
0
Moore
Mealy
0/0
Format:
Arc = input X
Node = state/output Q
Format:
Arc = input X / mealy output Y
Node = state
State
Output
Input
Basic Format:

## Slide 58: Example 1 - Circuit w/o Primary Inputs
Z
Q0
D
Q
Q
D
Q
Q
CLK
Y
D0
Q1
D1
Excitation: D0 = (Q0 + Q1’)’ = Q0’ · Q1
D1 = Q0
Output: Y = Q0 · Q1
Z = Q1 Thus, Moore machine

## Slide 59: Example 1 - Equations
Excitation
D0 = Q0’ · Q1
D1 = Q0
Transition
Q0(t+1) = D0 = Q0’ · Q1
Q1(t+1) = D1 = Q0
Characteristic
Q0(t+1) = D0
Q1(t+1) = D1
Output
Y = Q0 · Q1
Z = Q1

## Slide 60: Example 1 - Tables
State Table:
Q1 Q2 Y Z
0 0 00 0 0
0 1 10 0 1
1 0 01 0 0
1 1 01 1 1
State Table w/named states:
S Y Z
A A 0 0
B C 0 1
C B 0 0
D B 1 1
Q1(t+1)Q2(t+1)
No inputs!
S(t+1)
Transition
Q0(t+1) = D0 = Q0’ · Q1
Q1(t+1) = D1 = Q0

## Slide 61: Example 1 - State Diagram
B
A
00
01
D
11
C
00
A,D Unreachable, Only B,C are useful.
Therefore, only 1 flip-flop is needed.
Format:
Arc = no input
Node = state/outputs YZ

## Slide 62: Example 2 - State Machine with D Flip-flops
D Q
CLK Q
D Q
CLK Q
D Q
CLK Q
X
Y
/Q2
Q0
Q1
CLK
D0
D1
D2
Q0
Q1
Q2
Z1
/Z2
State Memory
Input Logic
F
Output Logic
G
/Q2

## Slide 63: Example 2 - Equations
Excitation
D0 = X Y’Q2
D1 = X Q0
D2 = Y’ + Q1
Transition
Q0(t+1) = D0 = X Y’ Q2’
Q1(t+1) = D1 = X Q0
Q2(t+1) = D2 = Y’ + Q1
Characteristic
Q0(t+1) = D0
Q1(t+1) = D1
Q2(t+1) = D2
Output
Z1 = X Q0 + Q1’
/Z2= (Q1 Q2)’

## Slide 64: Example 2 - Two-Dimensional State table
state XY
name Q2 Q1 Q0 00 01 11 10
A= 0 0 0 100, 11 000, 11 000, 11 101, 11
B= 0 0 1 100, 11 000, 11 010, 11 111, 11
C= 0 1 0 100, 01 100, 01 100, 01 101, 01
D= 0 1 1 100, 01 100, 01 110, 11 111, 11
E= 1 0 0 100, 11 000, 11 000, 11 100, 11
F= 1 0 1 100, 11 000, 11 010, 11 110, 11
G= 1 1 0 100, 00 100, 00 100, 00 100, 00
H= 1 1 1 100, 00 100, 00 110, 10 110,10
Q2(t+1) Q1(t+1) Q0(t+1), Z1 /Z2
(Next State, Outputs)
  Transition Equations
  Q0(t+1) = D0 = X Y’ Q2’
  Q1(t+1) = D1 = X Q0
  Q2(t+1) = D2 = Y’ + Q1
X Y Q2 Q1 Q0
1 0 0 - -
1 - - - 1
- 0 - - - or
- - - 1 -
  Output Equations
  Z1 = X Q0 + Q1’
  /Z2= (Q1 Q2)’

## Slide 65: Example 2 - Named State / Output table
XY
S 00 01 11 10
A E, 11 A, 11 A, 11 F, 11
B E, 11 A, 11 C, 11 H, 11
C E, 01 E, 01 E, 01 F, 01
D E, 01 E, 01 G, 11 H, 11
E E, 11 A, 11 A, 11 E, 11
F E, 11 A, 11 C, 11 G, 11
G E, 00 E, 00 E, 00 E, 00
H E, 00 E, 00 G, 10 G,10
S(t+1), Z1 /Z2

## Slide 66: Example 2 - State Diagram
A
E
C
D
H
B
F
G
Y (11)
(11) X’ Y
X Y (11)
X’ Y’
(11)
X Y’
(11)
X’Y’
(11)
XY’
(11)
XY’
(01)
X’+Y
(01)
Different format
Arc: input expression (outputs) = expression (Z1 /Z2)
B
A
x y’ (11)
x’ y (10)
Also possible:
Same transition,
but different outputs
XY’
(11)
X’
(01)
XY
(11)
Incomplete!

## Slide 67: Analysis of J-K Flip-Flop State Machines
There are two excitation equations per flip-flop (J , K)
The characteristic equation : Q(t+1) = J·Q(t)’ + K’·Q(t)
Use the same analysis procedure shown previously

## Slide 68: Example 3 - State Machine with J-K Flip-flops
J
K
CLK
X
Y
Z
Mealy Output:
Z = X·Q1 + Q2
Q1
Q2
J1
K1
J2
K2
J
K
Q
Q
Q
Q

## Slide 69: Example 3 - Equations
Excitation
J1 = X
K1 = X·Y
J2 = X’
K2 = 0
Transition
Q1(t+1) = X·Q1’ + (X·Y)’ ·Q1 = X·Q1’ + X’·Q1 + Y’·Q1
Q2(t+1) = X’·Q2’ + 0’·Q2 = X’·Q2’ + Q2
Characteristic
Q(t+1)= J·Q’ + K’·Q
Q1(t+1) = J1·Q1’ + K1’·Q1
Q2(t+1) = J2·Q2’ + K2’·Q2
Mealy Output
Z = X·Q1 + Q2

## Slide 70: Example 3 - State Table
XY
S Q1 Q2 00 01 11 10
A 0 0 01,0 01,0 10,0 10,0
B 0 1 01,1 01,1 11,1 11,1
C 1 0 11,0 11,0 00,1 10,1
D 1 1 11,1 11,1 01,1 11,1
Q1(t+1) Q2(t+1), Z
Transition
Q1(t+1) = X·Q1’ + (X·Y)’ ·Q1 = X·Q1’ + X’·Q1 + Y’·Q1
Q2(t+1) = X’·Q2’ + 0’·Q2 = X’·Q2’ + Q2
Mealy Output
Z = X·Q1 + Q2

## Slide 71: Example 3 - Named State/Output Table
XY
S 00 01 11 10
A B,0 B,0 C,0 C,0
B B,1 B,1 D,1 D,1
C D,0 D,0 A,1 C,1
D D,1 D,1 B,1 D,1
S(t+1), Z

## Slide 72: Example 3 - State Diagram
A
B
C
D
00,01,10
1
10
1
00,01
1
00,01
0
11
1
10,11
0
00,01
0
11
1
10,11
1
Arc Format:
inputs xy
output z

## Slide 73: Example 3 - State Diagram
A
B
C
D
(XY)’
1
XY’
1
X’
1
X’
0
XY
1
X
0
X’
0
XY
1
X
1
Arc Format:
Transition Expression
output
For each state/input combination there must be exactly one next-state (and output).
Mutual Exclusion: No more than one transition arc from any state can be satisfied by
any input assignment
All Inclusion: At least one transition arc must exist from any state for any input
assignment

## Slide 74: Timing Analysis
All digital devices have associated propagation delays (min,max)
Sequential devices have setup and hold times that must be satisfied to avoid metastable behavior
Providing a synchronous clock simplifies timing analysis
  All devices produce effects within a well-defined range
At what speeds will a device function?
  One transition per clock
  What is the maximum clock rate?
Sequential devices require the following timing documentation:
  Maximum propagation delay (clock to output)
  Minimum propagation delay (clock to output)
  Setup time (input before clock)
  Hold time (input after clock)

## Slide 75: 74LS74 Data Sheet Timing
Parameter Min Max Units
tW Pulse Width - Clock High 18 ns
- Preset Low 15 ns
- Clear Low 15 ns
tSU Setup Time 20 ns
tH Hold Time 0 ns
fMAX Max Clock Frequency 20 MHz
tPLH Prop Delay, Clock-to-Q 35 ns
tPLH Prop Delay, Preset-to-Q 35 ns
tPLH Prop Delay, Clear-to-Q 35 ns

## Slide 76: Clocked Synchronous State-machine Structure
Next-state
Logic
F
State
Memory
clock
Output
Logic
G
excitation
inputs
clock
current state
outputs
(Mealy machine)
F, t_pd(max)
F, t_pd(min)
G, t_pd(max)
G, t_pd(min)
R, t_pd(max)
R, t_pd(min)
R, setup(max)
R, hold(max)
Calculate:

## Slide 77: Timing Diagram
CLOCK
flip-flop
outputs
tH
tL
tclk
tffpd
combinational
outputs
flip-flop
inputs
tcomb
setup-time margin
tsetup
thold

## Slide 78: Calculating Sequential Device Timing Specs.
Calculate the delay from clock edge to worst-case primary output:
  t_pd(min) = R,t_pd(min) + G,t_pd(min)
  t_pd(max) = R,t_pd(max) + G,t_pd(max)
Calculate the worst-case setup time for any input:
  t_setup = F,t_pd(max) + R,setup(max)
Calculate the worst-case hold time for any input:
  t_hold = R,hold(max) - F,t_pd(min)
Calculate the maximum clock rate by finding the minimum period:
  min. period = R,t_pd(max) + F,t_pd(max) + R,setup(max)
Make certain that the device works!
  R,t_pd(min) + F,t_pd(min) > R,hold(max)

## Slide 79: Synchronous System Example
tpd,comb = 2 ns (min) to 20 ns (max) tpd,ff = 3 ns (min) to 15 ns (max)
tsetup= 5 ns
thold = 4 ns
Setup/Hold Time: tsetup = 20 + 5; thold = 4 - 2 = 2 ns
Max Frequency? tclk,min >= 15 + 20 + 5 = 40 ns,
fmax <= 25 MHz (40ns)-1 = 25 MHz
Setup margin @ 10 MHz? 100 - 40 = 60 ns
Hold Margin? (3 + 2) - 5 = 0 ns
Combinational
logic
State
Devices
Q3
Q2
Q1
in1
in2