## Slide 1: Design Methodologies

## Slide 2: The Design Problem
Source: sematech97
A growing gap between design complexity and design productivity

## Slide 3: Design Methodology
Design process traverses iteratively between three abstractions: behavior, structure, and geometry
More and more automation for each of these steps

## Slide 4: Design Analysis and Verification
Accounts for largest fraction of design time
More efficient when done at higher levels of abstraction - selection of correct analysis level can account for multiple orders of magnitude in verification time
Two major approaches:
  Simulation
  Verification

## Slide 5: Digital Data treated as Analog Signal
Circuit Simulation
Both Time and Data treated as Analog Quantities
Also complicated by presence of non-linear elements
(relaxed in timing simulation)

## Slide 6: Representing Data as Discrete Entity
Discretizing the data using
switching threshold
The linear switch model
of the inverter

## Slide 7: Circuit versus Switch-Level Simulation
Circuit
Switch

## Slide 8: Structural Description of Accumulator
Design defined as composition of
register and full-adder cells (“netlist”)
Data represented as {0,1,Z}
Time discretized and progresses with
unit steps
Description language: VHDL
Other options: schematics, Verilog

## Slide 9: Behavioral Description of Accumulator
Design described as set of input-output
relations, regardless of chosen
implementation
Data described at higher abstraction
level (“integer”)

## Slide 10: Behavioral simulation of accumulator
Integer data
Discrete time
(Synopsys Waves display tool)

## Slide 11: Timing Verification
(Synopsys-Epic Pathmill)
Critical path
Enumerates and rank
orders critical timing paths
No simulation needed!

## Slide 12: Issues in Timing Verification
False Timing Paths

## Slide 13: Implementation Methodologies

## Slide 14: Custom Design – Layout Editor
Magic Layout Editor
(UC Berkeley)

## Slide 15: Symbolic Layout
Stick diagram of inverter
Dimensionless layout entities
Only topology is important
Final layout generated by “compaction” program

## Slide 16: Cell-based Design (or standard cells)
Routing channel
requirements are
reduced by presence
of more interconnect
layers

## Slide 17: Standard Cell — Example
[Brodersen92]

## Slide 18: Standard Cell - Example
3-input NAND cell
(from Mississippi State Library)
characterized for fanout of 4 and
for three different technologies

## Slide 19: Automatic Cell Generation
Random-logic layout
generated by CLEO
cell compiler (Digital)

## Slide 20: Module Generators — Compiled Datapath

## Slide 21: Macrocell Design Methodology
Macrocell
Interconnect Bus
Routing Channel
Floorplan:
Defines overall
topology of design,
relative placement of
modules, and global
routes of busses,
supplies, and clocks

## Slide 22: Macrocell-Based Design Example
Video-encoder chip
[Brodersen92]
SRAM
SRAM
Routing Channel
Data paths
Standard cells

## Slide 23: Gate Array — Sea-of-gates
Uncommited
Cell
Committed
Cell (4-input NOR)

## Slide 24: Sea-of-gate Primitive Cells
Using oxide-isolation
Using gate-isolation

## Slide 25: Sea-of-gates
Random Logic
Memory
Subsystem
LSI Logic LEA300K
(0.6 m CMOS)

## Slide 26: Prewired Arrays
Categories of prewired arrays (or field-programmable devices):
Fuse-based (program-once)
Non-volatile EPROM based
RAM based

## Slide 27: Programmable Logic Devices
PLA
PROM
PAL

## Slide 28: EPLD Block Diagram
Macrocell
Courtesy Altera Corp.
Primary inputs

## Slide 29: Field-Programmable Gate Arrays Fuse-based
Standard-cell like
floorplan

## Slide 30: Interconnect
Programming interconnect using anti-fuses

## Slide 31: Field-Programmable Gate Arrays RAM-based

## Slide 32: RAM-based FPGA Basic Cell (CLB)
Courtesy of Xilinx

## Slide 33: RAM-based FPGA
Xilinx XC4025

## Slide 34: Taxonomy of Synthesis Tasks

## Slide 35: Design for Test

## Slide 36: Validation and Test of Manufactured Circuits
Components of DFT strategy
Provide circuitry to enable test
Provide test patterns that guarantee reasonable
coverage
Goals of Design-for-Test (DFT)
Make testing of manufactured part swift and
comprehensive
DFT Mantra
Provide controllability and observability

## Slide 37: Test Classification
Diagnostic test
  used in chip/board debugging
  defect localization
“go/no go” or production test
  Used in chip production
Parametric test
  x  [v,i] versus x  [0,1]
  check parameters such as NM, Vt, tp, T

## Slide 38: Design for Testability
Exhaustive test is impossible or unpractical

## Slide 39: Problem: Controllability/Observability
Combinational Circuits:
  controllable and observable - relatively easy to determine test patterns
Sequential Circuits: State!
  Turn into combinational circuits or use self-test
Memory: requires complex patterns
  Use self-test

## Slide 40: Test Approaches
Ad-hoc testing
Scan-based Test
Self-Test
Problem is getting harder
  increasing complexity and heterogeneous combination of modules in system-on-a-chip.
  Advanced packaging and assembly techniques extend problem to the board level

## Slide 41: Generating and Validating Test-Vectors
Automatic test-pattern generation (ATPG)
  for given fault, determine excitation vector (called test vector) that will propagate error to primary (observable) output
  majority of available tools: combinational networks only
  sequential ATPG available from academic research
Fault simulation
  determines test coverage of proposed test-vector set
  simulates correct network in parallel with faulty networks
Both require adequate models of faults in CMOS integrated circuits

## Slide 42: Fault Models
    Most Popular - “Stuck - at” model
    , : x1 sa1
     : x1 sa0 or
    x2 sa0
     : Z sa1
Covers almost all (other)
occurring faults, such as
opens and shorts.

## Slide 43: Problem with stuck-at model: CMOS open fault
Sequential effect
Needs two vectors to ensure detection!
Other options: use stuck-open or stuck-short models
This requires fault-simulation and analysis at the switch or transistor level - Very expensive!

## Slide 44: Problem with stuck-at model: CMOS short fault
Causes short circuit between
Vdd and GND for A=C=0, B=1
Possible approach:
Supply Current Measurement (IDDQ)
but: not applicable for gigascale integration

## Slide 45: Path Sensitization
Techniques Used: D-algorithm, Podem
Goals: Determine input pattern that makes a fault
controllable (triggers the fault, and makes its impact
visible at the output nodes)
sa0
1
1
0
1
1
1
0
1
Fault propagation
Fault enabling

## Slide 46: Ad-hoc Test
Inserting multiplexer improves testability

## Slide 47: Scan-based Test

## Slide 48: Polarity-Hold SRL (Shift-Register Latch)
Introduced at IBM and set as company policy

## Slide 49: Scan-Path Register

## Slide 50: Scan-based Test —Operation

## Slide 51: Scan-Path Testing
Partial-Scan can be more effective for pipelined datapaths

## Slide 52: Boundary Scan (JTAG)
Board testing becomes as problematic as chip testing

## Slide 53: Self-test
Rapidly becoming more important with increasing
chip-complexity and larger modules

## Slide 54: Linear-Feedback Shift Register (LFSR)
Pseudo-Random Pattern Generator

## Slide 55: Signature Analysis
Counts transitions on single-bit stream
 Compression in time

## Slide 56: BILBO

## Slide 57: BILBO Application

## Slide 58: Memory Self-Test
Patterns: Writing/Reading 0s, 1s,
Walking 0s, 1s
Galloping 0s, 1s